## Slide 1
Gaze: Hands-Free Cursor Control from a Webcam
Measuring the on-screen accuracy of a calibrated, webcam-only eye tracker (Linux, Wayland port)
[Author name(s)] · ASDRP · Research poster, due Oct 11
Abstract
Eye tracking can give people with limited motor control a way to use a computer without their hands, but most systems need dedicated infrared hardware. Gaze estimates where a user is looking from an ordinary webcam, calibrates that signal to the screen, and drives the real system cursor. We built a Linux (Wayland) port and an accuracy test that logs each target's predicted position. Across 7 valid runs (83 targets) the mean error was 164 px (median 124 px) on a 1920×1080 display, and 70% of targets landed within 200 px.
Motivation
Commercial gaze trackers are costly and tied to specific hardware. A webcam-only tool that runs locally keeps video on the device and works on the laptop a person already owns. The open question is whether its accuracy is good enough to hit real interface targets.
Methods
Face and iris landmarks from MediaPipe FaceLandmarker (Lugaresi et al., 2019), with head pose.
One-Euro smoothing of the gaze signal.
Calibration: a 5×5 grid, a dwell window per point, then smooth-pursuit passes. A ridge regression maps eye features to screen position.
Accuracy test: 12 shuffled targets per pass, 600 ms settling time per target, mean predicted position logged against the target.
Cursor control: macOS CoreGraphics, Linux X11 XTest, and Wayland RemoteDesktop portal (libei).
Results
Figure 1. Predicted gaze position for each target (+), all valid runs. Lines join each prediction to its target.
164 px
mean error
124 px
median error
70%
within 200 px
Figure 2. Cumulative distribution of error. Dashed lines mark 100 px and 200 px.
n = 83 targets, 7 runs. Two runs were excluded: one aborted after 2 points, one never held calibration (predictions stayed near x = 0.43).
Where the error is
Figure 3. Mean error (px) by screen region. The left column is worst.
Figure 4. Per-run error. Orange: earlier build; blue: Linux build. Run-to-run spread is large.
Discussion and limitations
Error was 100–250 px across most of the screen: enough for large controls, not small ones.
The earlier and Linux builds do not differ beyond run-to-run spread (mean 143 vs 180 px).
Left-edge targets averaged 211–246 px; centre columns 98–136 px.
Few runs, one participant, one display: results are descriptive. Viewing distance was not recorded, so no visual angle.
Reference: Lugaresi, C. et al. (2019). MediaPipe: A Framework for Building Perception Pipelines. arXiv:1906.08172. Code and data: the Gaze repository (analysis/).